ELECTROMAGNETIC INDUCTION
(Y&F Chapters 30, 31; Ohanian Chapter 32)

This handout covers:

- Motional emf and the electric generator

- Electromagnetic Induction and Faraday’s Law

- Lenz’s Law

- Induced electric field

- Inductance

- Magnetic energy

The Electric and magnetic fields are inter-related

The electric and magnetic fields are not independent.  In fact:

- A changing magnetic field induces an electric field

- The reverse is also true: a changing electric field induces a magnetic 	field

To see how this occurs, we first consider MOTIONAL emf

Motional emf

## Consider a wire moving 
with velocity v in a magnetic 
field .

## Assume for simplicity that 
 and  are perpendicular

The electrons in the wire 
experience a force

## This produces a separation of 
charge with an excess of negative 
charge at one end and positive 
charge at the other.

## There is therefore an INDUCED 
emf between the two ends.

## Induced emf   ℰ  =  work done to move a unit positive charge from 
a to b against the magnetic force 		
																	F  = QvB  =  vB

Work done = (Force)(Distance)  (   	ℰ  =  vBL         MOTIONAL emf

The electric generator

## Assume that the ends of the wire are connected up through some external circuit (which we represent here by a simple resistor).

Current I flows and dissipates 
electrical power in R.

## Where does this power come from?

The current is due to electrons 
moving in the wire with some 
drift velocity velectron.

The electrons therefore experience 
a magnetic force

## This force OPPOSES the motion 
of the wire through the field.


The overall force on the wire is 	Fmag  = (F for all the electrons.

Recall:  	Force on a current-carrying wire in a magnetic field is  

				Fmag  = BIL.

So, the power delivered to the circuit comes from the effort needed to PUSH the wire through the magnetic field against this force.

The magnetic field thus acts as a mediator in the conversion of MECHANICAL ENERGY into ELECTRICAL ENERGY.

This is the principle of the ELECTRIC GENERATOR.

Exercise: Show that the power needed to move the wire through the magnetic field is equal to the power dissipated in the resistor.

Motional emf and magnetic flux

## Recall: 	ℰ = vBL

In a time dt, the conductor moves 
a distance vdt.

The area swept out is therefore

ds  = Lvdt

## The magnetic flux passing 
through this area is

d(  =  Bds  = BLvdt

## Therefore		  	(		ℰ =

## The induced emf is equal to the rate of sweeping out of magnetic flux

Note:  	1.  	This applies to ANY shape of conductor in ANY magnetic field.

			2.		The same equation applies to a stationary conductor in a
 					changing magnetic field.

Faraday's law of induction

The induced emf around any closed path in a magnetic field is equal to minus the rate of change of the magnetic flux intercepted by the path:

					ℰ  = 							Why the negative sign?

Lenz's law

This is represented by the negative sign in the above equation for the induced emf.

The induced emf is in such a direction as to OPPOSE the change in magnetic field that produces it.

If (  is increasing then ℰ 
causes current to flow so 
as to generate a magnetic 
field which OPPOSES (.

If (  is decreasing then ℰ 
causes current to flow so 
as to generate a magnetic 
field which SUPPORTS (.

Induced electric field

Consider again a wire moving in a 
magnetic field.

Look at the situation from the point 
of view of someone who moves

along with the wire:

v  =  0   (  there is no magnetic force

Therefore, this observer interprets the 
force acting on the electrons in the wire 
as being due to an INDUCED ELECTRIC 
FIELD.

(			around the closed path shown (  0.

(		The induced electric field is not conservative.

Faraday's Law is usually written in this form:


							FARADAY'S	 LAW
													MAXWELL'S 3rd EQUATION

In words:  The line integral of the electric field around a closed path is equal to minus the rate of change of magnetic flux through the path

Mutual inductance 

Faraday's Law (  a changing  (  induced emf

Consider two nearby circuits:

Changing current in Circuit 1

Changing magnetic field 
through Circuit 2

Induced emf in Circuit 2



Current flows in Circuit 2

Let I1(t) create magnetic field B1(t).	
Let (21  be the flux through circuit 2 due to I1

Clearly, B1 (  I1, 	so 		(21  ( I1

DEFINITION:  The constant of proportionality between (21 and I1 is called the MUTUAL INDUCTANCE:

From Faraday’s Law, the induced emf is given by		ℰ21  = -M21

Note:

- M21  depends on the shape, size, numbers of turns and relative positions of the two circuits

- M21  =  M12  so we need only use M as the symbol for mutual inductance

- Ohanian uses L for mutual inductance

- In the SI system, inductance is measured in Henrys (H)

1 H = Inductance that produces an emf of 1 Volt for a rate of change of current of 1 A s-1

1 H  (  1 V s A-1

- The usual unit for (o is H m-1

Self inductance 

Even a single circuit produces a magnetic field that passes through the circuit itself.

So, if I changes (   changes ( ( changes  (  induced emf

Definition:	SELF INDUCTANCE

Inductance and Lenz’s law

ℰ21  = -M  or   -L

Recall: The negative sign represents Lenz’s Law: the emf causes current to flow so as to oppose the change in flux that produces it.

If ( is                                 then ℰ will cause current to flow so as to create

a magnetic field that 							 (.

Procedure for finding inductance

- Assume that a current I flows in (one of the) circuit(s)

- Find the magnetic field (e.g., use Ampere’s Law)

- Find the magnetic flux linked

- Put M or L equal to (/I

Examples:
1.		Mutual inductance of two long coaxial solenoids

2.		Self inductance of a long solenoid
See lecture notes

Energy storage in inductors

Recall:

Similarly:

To find the energy stored in an inductor:

Let current in the inductor i = 0 initially

Apply external emf  (  current increases at rate 		

This leads to a back emf  												ℰb  = -L

To make current flow, the required external emf is	 	ℰext  =  L
The externally applied power is therefore						P  =   ℰexti   = Li

The work done to increase the current from 0 to I is therefore

U  =   			(  		U  =  ½ LI2

Where is the stored energy?  It is in the MAGNETIC FIELD.

Recall:  For a solenoid of length a, radius R, n turns per unit length:

L  =  (R2(on2a			B  = (onI

U   =   ½ LI2   =   =

Therefore U  =  

The ENERGY DENSITY OF THE MAGNETIC FIELD is therefore


 		This holds generally, for any magnetic field.

# Text boxes

a

B (out)

v

L

b

F  =  -e(v x B)

B (out of page)

v

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

Energy stored in an inductor “charged” with current I

Because:  changing current (  changing   (  induced emf which opposes attempt to change current (called a “back emf”)

Umag  = ?

Uelec  =  ½ CV2

(

(

Storing

potential

energy

Doing

work

Making current flow in an inductor

(

(

Storing

potential

energy

Doing

work

v x B

Putting a charge

on a capacitor

- i1(t) decreases

- (21 decreases

- Induced emf in circuit 2 
	drives current i2(t)

- I2(t) generates  which 	SUPPORTS

i2(t)

B2(t)

i1(t)

B1(t)

Circuit 2

Circuit 1

i2(t)

- i1(t) increases

- (21 increases

- Induced emf in circuit 2 
	drives current i2(t)

- I2(t) generates which 	OPPOSES

B2(t)

i1(t)

B1(t)

Circuit 2

Circuit 1

OPPOSES

SUPPORTS

INCREASING

DECREASING

L

I

I1

B1

Circuit 2

+ + +

v

- - -

Circuit 1

E

v

B (out of page)

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

L

Current due to

induced emf

Binduced supports B

B (decreasing)

Current due to

induced emf

Binduced opposes B

B (increasing)

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.		.	.	.	.	.

B (out of page)

. 	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.

R

F  =  -e(velectron x B)

B (out)

v

velectron

B (out of page)

v

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.	.	.	.	.	.	.

. 	.	.	.	.	.	.	.	.		.	.	.	.	.

vdt